# MSDS     Material Safety Data Sheet

RCS Chemicals

Plot No. 3, I.D.A., KADAPA, Andhra Pradesh, India

Regd. Office : 20/584-1, Namaste Board Lane,

Kadapa – 516 001. Andhra Pradesh, India.

Ph : +91 8562 243179, +91 8562 251179

Fax : +91 8562 246179

# BARIUM SULFATE  (Barytes Powder)

## 1. Product Identification

Synonyms:  barium salt; barytes; blanc fixe; barite 
CAS No. : 7727-43-7

Molecular Weight: 233.39 
Chemical Formula: BaSO4 
Product Codes: 
J.T. Baker: 1030, 1040, 1041 
Mallinckrodt: 0991, 4518, 8821

## 2. Composition/Information on Ingredients

Ingredient                     	CAS No         Percent

-------------------------------   ------------   ------------

Barium Sulfate           	       7727-43-7      97 – 100%

## 3. Hazards Identification

Emergency Overview

-------------------------- 
As part of good industrial and personal hygiene and safety procedure, avoid all unnecessary exposure to the chemical substance and ensure prompt removal from skin, eyes and clothing.

SAF-T-DATA(tm) Ratings (Provided here for your convenience) 
------------------------------------------------------------------------------------------------------- 
Health Rating: 1 - Slight 
Flammability Rating: 0 - None 
Reactivity Rating: 1 - Slight 
Contact Rating: 1 - Slight 
Lab Protective Equip: GOGGLES; LAB COAT; PROPER GLOVES 
Storage Color Code: Green (General Storage) 
----------------------------------------------------------------------------------------------------------- 

Potential Health Effects 
---------------------------------- 

Inhalation		:	Not expected to be a health hazard. 
Ingestion		:	Not expected to be a health hazard. 
Skin Contact		:	No adverse effects expected. 
Eye Contact		:	No adverse effects expected but dust may cause

mechanical irritation.

Chronic Exposure	: 	Long term inhalation of dust may lead to deposition in lungs in sufficient quantities to produce baritosis - a benign pneumoconiosis. This produces a radiological picture even though symptoms and abnormal signs may not be present.

Aggravation of Pre-existing Conditions  :  No information found.

## 4. First Aid Measures

Inhalation	:	Remove to fresh air. Get medical attention for any breathing difficulty. 
Ingestion	:	Give several glasses of water to drink to dilute. If large amounts were

swallowed, get medical advice.

Skin Contact	: 	Wash exposed area with soap and water. Get medical advice if

irritation develops.

Eye Contact	: 	Wash thoroughly with running water. Get medical advice if irritation

develops.

## 5. Fire Fighting Measures

Fire	:	Not considered to be a fire hazard.

Explosion	:	Not considered to be an explosion hazard.

Fire Extinguishing Media	:	Use any means suitable for extinguishing surrounding fire.

Special Information	:	In the event of a fire, wear full protective clothing and NIOSH-approved self-contained breathing apparatus with full facepiece operated in the pressure demand or other positive pressure mode.

## 6. Accidental Release Measures

Ventilate area of leak or spill. Wear appropriate personal protective equipment as specified in Section 8. Spills: Sweep up and containerize for reclamation or disposal. Vacuuming or wet sweeping may be used to avoid dust dispersal.

## 7. Handling and Storage

Keep in a tightly closed container. Protect from physical damage. Store in a cool, dry, ventilated area away from sources of heat, moisture and incompatibilities. Containers of this material may be hazardous when empty since they retain product residues (dust, solids); observe all warnings and precautions listed for the product.

## 8. Exposure Controls/Personal Protection

Airborne Exposure Limits: 
-OSHA Permissible Exposure Limit (PEL):
15 mg/m3 total dust, 5 mg/m3 respirable dust
-ACGIH Threshold Limit Value (TLV):
10 mg/m3 (TWA) 
Ventilation System: 
In general, dilution ventilation is a satisfactory health hazard control for this substance. However, if conditions of use create discomfort to the worker, a local exhaust system should be considered.

Personal Respirators (NIOSH Approved):

If the exposure limit is exceeded and engineering controls are not feasible, a half facepiece particulate respirator (NIOSH type N95 or better filters) may be worn for up to ten times the exposure limit or the maximum use concentration specified by the appropriate regulatory agency or respirator supplier, whichever is lowest.. A full-face piece particulate respirator (NIOSH type N100 filters) may be worn up to 50 times the exposure limit, or the maximum use concentration specified by the appropriate regulatory agency, or respirator supplier, whichever is lowest. If oil particles (e.g. lubricants, cutting fluids, glycerine, etc.) are present, use a NIOSH type R or P filter. For emergencies or instances where the exposure levels are not known, use a full-facepiece positive-pressure, air-supplied respirator. WARNING: Air-purifying respirators do not protect workers in oxygen-deficient atmospheres.

Skin Protection:

Wear protective gloves and clean body-covering clothing.

Eye Protection:

Use chemical safety goggles. Maintain eye wash fountain and quick-drench facilities in work area.

## 9. Physical and Chemical Properties

Appearance					:	Fine, white powder. 
Odor						: 	Odorless. 
Solubility					:	Insoluble in water. 
Specific Gravity				:	4.5 @ 15 (59F) 
pH						:	5% in water is neutral to litmus. 
% Volatiles by volume @ 21C (70F)		:	0 
Boiling Point					:	1600C (2912F) Decomposes. 
Melting Point					:	1580C (2876F) 
Vapor Density (Air=1)				:	No information found. 
Vapor Pressure (mm Hg)			:	No information found. 
Evaporation Rate (BuAc=1)			:	No information found.

## 10. Stability and Reactivity

Stability					:	Stable under ordinary conditions of use

and storage.

Hazardous Decomposition Products		:	Burning may produce sulfur oxides. 
Hazardous Polymerization			:	Will not occur. 
Incompatibilities				:	Aluminum, phosphorus. 
Conditions to Avoid				:	Dusting and incompatibles.

## 11. Toxicological Information

No LD50/LC50 information found relating to normal routes of occupational exposure.

--------\Cancer Lists\--------------------------------------------------

---NTP Carcinogen---

Ingredient                         Known    Anticipated    IARC Category

--------------------------------   -----    -----------    -------------

Barium Sulfate (7727-43-7)              No          No            None

## 12. Ecological Information

Environmental Fate		:	This material may bioaccumulate to some extent. 
Environmental Toxicity	:	No information found.

## 13. Disposal Considerations

Whatever cannot be saved for recovery or recycling should be managed in an appropriate and approved waste disposal facility. Processing, use or contamination of this product may change the waste management options. State and local disposal regulations may differ from federal disposal regulations. Dispose of container and unused contents in accordance with federal, state and local requirements.

## 14. Transport Information

Not regulated. (Non-hazardous for air, sea and road freight)

## 15. Regulatory Information

--------\Chemical Inventory Status - Part 1\-----------------------------

Ingredient                                   TSCA  EC   Japan  Australia

-------------------------------------------  ----  ---  -----  ---------

Barium Sulfate (7727-43-7)                    Yes  Yes   Yes      Yes

--------\Chemical Inventory Status - Part 2\-----------------------------

--Canada--

Ingredient                                   Korea  DSL   NDSL  Phil.

-------------------------------------------  -----  ---   ----  -----

Barium Sulfate (7727-43-7)                    Yes   Yes   No     Yes

--------\Federal, State & International Regulations - Part 1\--------------

-SARA 302-    ------SARA 313------

Ingredient                                 RQ    TPQ     List  Chemical Catg.

--------------------------------------  ---   -----   ----  --------------

Barium Sulfate (7727-43-7)               No    No      No         No

-------\Federal, State & International Regulations - Part 2\----------------

-RCRA-    -TSCA-

ingredient                                 CERCLA     261.33     8(d)

----------------------------------------  ------     ------    ------

Barium Sulfate (7727-43-7)                 No         No         No

Chemical Weapons Convention:  No     TSCA 12(b):  No     CDTA:  No

SARA 311/312:  Acute: Yes      Chronic: No   Fire: No  Pressure: No

Reactivity: No          (Pure / Solid)

Australian Hazchem Code: None allocated.

Poison Schedule: None allocated.

WHMIS: 
This MSDS has been prepared according to the hazard criteria of the Controlled Products Regulations (CPR) and the MSDS contains all of the information required by the CPR.

## 16. Other Information

NFPA Ratings: Health: 0 Flammability: 0 Reactivity: 0 
Label Hazard Warning : 
As part of good industrial and personal hygiene and safety procedure, avoid all unnecessary exposure to the chemical substance and ensure prompt removal from skin, eyes and clothing. 
Label Precautions	: 	None
Label First Aid	: 	Not applicable
Product Use		:	Laboratory Reagent