# MSDS     Material Safety Data Sheet

Chaitanya Chemicals

126, Rami Reddy Kottalu, Vallur (M), Kadapa District, A.P., India

Regd. Office : 20/584-1, Namaste Board Lane, Kadapa – 516 001. A.P. India.

Ph : +91 8562 243179, +91 8562 251179    Fax : +91 8562 246179

Email : info@chaitanyachemials.com  Website : www.chaitanyachemicals.com

# SODIUM SULPHIDE FLAKES

CAS # 1313-82-2 SODIUM SULFIDE FLAKES

HAZARD IDENTIFICATION
====================================================================

Route Of Entry Inds - 	Inhalation: YES Skin: YES Ingestion: YES

Carcinogenicity Inds - 	NTP: NO IARC: NO OSHA: NO

Health Hazards Acute And Chronic: FOR ING 1:ACUTE:INHAL:DUSTS MAY CAUSE SEV MUC MEMB IRRIT W/COUGH, CHOKE, PAIN IN NOSE, MOUTH & THROAT & BURNS OF MUC MEMB. PULM EDEMA MAY DEVELOP, OFTEN W/LATENT PERIOD OF 5-72 HRS. CNTCT W/ MOISTURE IN AIR/MUC MEMB MAY RELS HYDROGEN SULFID E GAS. SYMP:SHORTNESS OF BRTH, OFLACTORY PARALYSIS, HDCH, NAUS, (EFTS OF OVEREXP

Explanation of Carcinogenicity: NOT RELEVANT

Signs and Symptoms of Overexposure: HLTH HAZ:VOMIT, DIZZ, UNCON & DEATH FROM RESP PARALYSIS. SKIN:SEV IRRIT, PAIN & POSS BURNS. APPLICATN OF 340 MG/KG OF TRIHYDRATE WAS LETHAL TO 9 OF 10 RABBITS. EYES:SEV IRRIT W/REDNESS, PAIN, BLURRED VISION & BURNS WHICH ARE SLOW HEALING. B LINDNESS MAY RSLT. CNTCT MAY CAUSE RELS OF HYDROGEN SULFIDE CAUSING (ING 3)

Medical Conditions Aggravated by Overexposure: NONE SPECIFIED BY MANUFACTURER.

===================================================================

FIRST AID
=======================================================================

INHAL:REMOVE TO FRESH AIR IMMED. IF BRTHG STOPPED, GIVE ARTF RESP. MAINTAIN AIRWAY & BLOOD PRESS & ADMIN O2 IF AVAIL. KEEP WARM & @ REST. TREAT SYMPTOMATICALLY & SUPPORTIVELY. ADMIN OF O2 SHOULD BE PERFORMED BY QUALIFIED PERS. GET MED ATTN IMMED. SKIN:REMOVE CONTAMD CLTHG & SHOES. IMMED WASH AREA W/SOAP/MILD DETERGENT & LG AMT WATER UNTIL NO EVIDENCE OF CHEM REMAINS (@ LEAST 15-20 MIN). (ING 11)

=======================================================================
FIRE FIGHTING MEASURES
=======================================================================
Flash Point Text	: 	N/K

Auto Ignition Temperature Text: 

Lower Limits: N/K Upper Limits: N/K

Extinguishing Media: DRY CHEMICAL, CARBON DIOXIDE, WATERSPRAY OR REGULAR FOAM. FOR LARGER FIRES, USE WATER SPRAY, FOG OR REGULAR FOAM.

Fire Fighting Procedures: USE NIOSH/MSHA APPRVD SCBA & FULL PROT EQUIP (FP N). MOVE CNTNR FROM FIRE AREA IF YOU CAN DO W/OUT RISK. APPLY COOLING WATER TO SIDES OF CNTNRS THAT (SUPDAT)

Unusal Fire/Explosion Hazard: SLIGHT FIRE HAZARD WHEN EXPOSED TO HEAT OR FLAME. DUST-AIR MIXTURES MAY IGNITE OR EXPLODE.

=======================================================================
RELEASE MEASURES
=======================================================================

Spill Release Procedures: OCCUP SPILL: DO NOT TOUCH SPILLED MATL. STOP LEAK IF YOU CAN DO W/OUT RISK. SM SPILLS:TAKE UP W/SAND/OTHER ABSORB MATL & PLACE INTO CNTNRS FOR LATER DISP. SM DRY SPILLS:W/CLEAN SHOVEL PLACE MATL IN CLEAN, DRY CNTNR & COVER. MOVE CNTNR FROM (ING 21)

Neutralizing Agent: NONE SPECIFIED BY MANUFACTURER.

Waste Disposal Methods: OBSERVE ALL FEDERAL, STATE & LOCAL REGULATIONS WHEN STORING OR DISPOSING OF THIS SUBSTANCE.

=======================================================================
HANDLING AND STORAGE

=======================================================================
STORE IN COOL, DRY PLACE. KEEP CNTNR TIGHTLY CLOSED WHEN NOT IN USE. STORE AWAY FROM INCOMPATIBLE SUBSTANCES. MAY BURN BUT DOES NOT IGNITE READILY.

====================================================================

EXPOSURE CONTROLS/PERSONAL PROTECTION
====================================================================

Respiratory Protection: FOLLOWING RESP RECOM & RANKED IN ORDER FROM MIN TO MAX RESP PROT. SELECTION MUST BE BASED ON CONTAM LEVELS, SPECIFIC OPERATION, MUST NOT > WORKING LIM OF RESP & BE NIOSH/MSHA APPRVD. ANY TYPE C SUPPLIED AIR RESP W/FULL FCPIECE IN (ING 23)

Ventilation: PROVIDE LOCAL EXHAUST OR PROCESS ENCLOSURE VENTILATION TO MEET PUBLISHED EXPOSURE LIMITS.

Protective Gloves: IMPERVIOUS GLOVES (FP N).

Eye Protection: SPLASH PROOF/DUST RESISTANT (ING 25)

Other Equipment: IMPERVIOUS CLTHG TO PREVENT ALL CNTCT. EYE WASH FOUNTAIN & QUICK DRENCH SHOWER WITHIN IMMED WORK AREA FOR

EMERGENCY USE.

Work Hygenic Practices: IMPERVIOUS CLTHG TO PREVENT ALL CNTCT. EYE WASH FOUNTAIN & QUICK DRENCH SHOWER WITHIN IMMED WORK AREA FOR EMERGENCY USE.

Supplemental Safety & Health: PH:ALKALINE IN SOLN. FIRE FIGHT PROC:ARE EXPOSED TO FLAMES UNTIL WELL AFTER FIRE IS OUT. STAY AWAY FROM ENDS OF TANKS. FLOOD W/WATER TO EXTING FIRE. AVOID CONTAM OF WATER SOURCES & SEWERS. STOP LEAK IF POSS W/OUT UNDUE HAZ. DO NOT BREATHE V AP & DUST.

====================================================================
PHYSICAL AND CHEMICAL PROPERTIES
====================================================================
HCC					: 	B3
Boiling Point: 				:	346F,174C
Melting/Freezing Point		:	197F,92C
Decomposition Temp			:	N/K
Vapor Pressure			: 	N/K

Vapor Density				: 	N/K
Specific Gravity			: 	1.858
PH					: 	SUPDAT
Viscosity				: 	N/P
Evaporation Rate & Reference	: 	N/K
Solubility in Water			: 	15% @ 20C
Appearance and Odor		: 	WHITE TO YELLOW FLAKES W/SLIGHT ODOR

OF ROTTEN EGGS.

Percent Volatiles by Volume		: 	N/K
Corrosion Rate			: 	N/K

====================================================================
STABILITY AND REACTIVITY
====================================================================
Stability Indicator			: 	YES
Stability Conditions to Avoid		: 	NONE SPECIFIED BY MANUFACTURER.
Materials to Avoid			: 	ACIDS, CARBON (PWDR), DIAZONIUM SALTS,

N,N DICHLOROMETHYLAMINE, OXIDIZERS (STRONG), SODIUM CARBONATE.

Hazardous Decomposition Products	: 	MAY INCLUDE TOXIC OXIDES OF SULFUR & SODIUM & TOXIC & FLAMMABLE HYDROGEN SULFIDE.

Hazardous Polymerization Products	: 	NO

Conditions to Avoid Polymerization	: 	NOT RELEVANT

====================================================================

TOXICOLOGICAL

N/P
====================================================================
ECOLOGICAL
====================================================================
N/P
====================================================================
DISPOSAL
====================================================================
OBSERVE ALL FEDERAL, STATE & LOCAL REGULATIONS WHEN STORING OR DISPOSING OF THIS SUBSTANCE.
====================================================================

TRANSPORTATION
====================================================================

N/P
====================================================================

REGULATORY
====================================================================

SARA Title III		:	N/P
Federal Regulatory	:	N/P
====================================================================